## Slide 1
Electric Vehicle Sensor Analytics
Predictive Machine Learning Dashboard for EV Performance, Safety & Battery Health
Turning raw OBD-II telemetry into actionable intelligence — without expensive hardware.
Python
Streamlit
Scikit-learn
XGBoost
Pandas
Plotly
Dataset: eVED (Electric Vehicle Energy Dataset) — 37 OBD-II telemetry columns, ~500K rows
CAP_PROJ_2 | Electric Vehicle Intelligence Platform | 2026

## Slide 2
The Problem
What is broken in today's EV ecosystem?
Range Anxiety & Hidden Drain
• EVs claim 300mi range — drops to 180mi on cold mountain drives
• Reactive climate control drains battery with zero intelligence
• No system proactively throttles power before battery-critical zones
Expensive Safety Hardware
• ADAS (cameras, radar, LIDAR) costs $3,000–$15,000 per vehicle
• Unavailable to most existing vehicles on the road today
• System failures in adverse weather (rain, fog) create false safety
Invisible Battery Degradation
• Drivers unknowingly destroy $15,000 batteries daily
• Dealerships only discover damage when battery completely fails
• No live feedback on chemical stress from aggressive driving events
CAP_PROJ_2 | Electric Vehicle Intelligence Platform

## Slide 3
Our Solution
An intelligent software layer on top of standard OBD-II sensor data
OBD-II Telemetry CSV
F1: HVAC Optimizer
Predicts power drain, throttles AC proactively
F2: Regen Braking
Predicts energy harvest from downhill segments
F3: Driver Eco-Score
Clusters driving style: Eco / Moderate / Aggressive
F4: Road Hazard Risk
Flags dangerous physics without cameras or radar
F5: Battery Health
Tracks micro-stress degradation events live
Dashboard & Visualization
Streamlit UI with live charts & ML predictions
Zero new hardware required — only the OBD-II port already present in every post-2008 vehicle.
CAP_PROJ_2 | Electric Vehicle Intelligence Platform

## Slide 4
Dataset & Technical Architecture
eVED — Electric Vehicle Energy Dataset
eVED Dataset Highlights
~500,000
Telemetry rows (1-sec OBD-II samples)
37
Sensor columns per row
5
Real EV trips across Michigan, USA
35+
Unique OBD-II parameters captured
100%
OBD-II only — no camera, no radar
Key Columns Used Across Features:
OAT [DegC] | Vehicle Speed [km/h] | HV Battery SOC [%] | HV Battery Current [A] | Gradient | Elevation Smoothed [m]Engine RPM | Absolute Load [%] | MAF [g/sec] | AC Power [Watts] | Heater Power [Watts] | Speed Limit [km/h]
ML Pipeline Architecture
1. CSV Upload
Raw OBD-II telemetry uploaded via Streamlit UI
2. Preprocessing
Column selection, imputation, outlier clipping, feature engineering
3. Train / Load Model
Auto-trains on first launch; loads saved .pkl on subsequent runs
4. Inference
Uploaded data passed through trained model for predictions
5. Visualization
Interactive Plotly charts: histograms, scatter, timeline, pie
6. Live Streaming (Sim)
Row-by-row simulation of real-time OBD-II sensor ingestion
CAP_PROJ_2 | Electric Vehicle Intelligence Platform

## Slide 5
Feature 1: Predictive HVAC Energy Optimizer
Model: Random Forest Regressor
Goal: Predict total HVAC power draw (Watts) from ambient + vehicle state so the system can proactively throttle HVAC before battery-critical zones — unlike reactive thermostats in current EVs.
Why Random Forest?
• Non-linear: HVAC follows a U-curve (cold=heater, hot=AC)
• Handles feature interactions (speed + OAT combined effects)
• Robust to sensor noise without overfitting
• 200 trees averaged = extremely stable predictions
Input Features
• OAT [DegC] — |r| ≈ 0.65 (primary driver)
• Vehicle Speed [km/h] — |r| ≈ 0.20
• HV Battery SOC [%] — |r| ≈ 0.12
• Elevation Smoothed [m] — |r| ≈ 0.10
• Gradient (road slope) — |r| ≈ 0.08
Key Dropped Columns
• Engine RPM — |r| < 0.06 (HVAC is electric, not belt-driven)
• Absolute Load — |r| < 0.05, 50% NaN
• HV Battery Current — target leakage risk
• AC Power [kW] — r=1.000 with Watts col (perfect collinear)
• Fuel Rate — ICE metric, irrelevant to EV HVAC
Engineered Features
• HVAC_Total_Watts = AC Power + Heater Power (target)
• Thermal_Load_Index = OAT x Speed (heat exchange proxy)
• Battery_Gradient_Constraint = SOC x Gradient
CAP_PROJ_2 | Electric Vehicle Intelligence Platform

## Slide 6
Feature 2: Gradient-Aware Regen Braking Predictor
Model: Gradient Boosting Regressor
Goal: Predict the magnitude of regenerative braking current recoverable from downhill or deceleration segments, enabling dynamic energy management and range extension.
How Regen Braking Works
• When decelerating, electric motor runs in reverse as a generator
• Converts kinetic energy → electricity → stored in HV Battery
• Negative HV Battery Current = energy flowing INTO the battery
• Current market: driver manually selects 'Standard' or 'Strong' mode
Why Gradient Boosting? (vs. Random Forest)
• Builds trees sequentially — each tree fixes errors of the last
• Better at capturing steep, sharp energy spikes (non-monotonic patterns)
• Learns complex interaction: high gradient + high speed = max regen
• 200 estimators, lr=0.1, max_depth=5, subsample=0.8
Input Features
• Gradient — slope determines max recoverable potential energy
• Vehicle Speed [km/h] — kinetic energy = 0.5 x m x v²
• HV Battery SOC [%] — regen disabled if SOC > 95% (full battery)
• Elevation Smoothed [m] — gravitational potential energy proxy
• Engine RPM — distinguishes EV vs. ICE braking modes
• HV Battery Current [A] — target variable (negative = charging)
Engineered Features
• Speed_Squared = Speed² (kinetic energy is proportional to v²)
• Gradient_Speed = Gradient x Speed (combined downhill momentum)
• Regen_Headroom = 95 - SOC (how much room left in the battery)
• Coasting_Flag = 1 if Speed > 0 and RPM < threshold (engine off drift)
CAP_PROJ_2 | Electric Vehicle Intelligence Platform

## Slide 7
Feature 3: Driver Behavior & Eco-Score Classifier
Model: KMeans Clustering → Random Forest Classifier
Goal: Automatically classify every driving moment as Eco, Moderate, or Aggressive using unsupervised clustering (no labelled data required), then train a fast classifier on top.
Two-Stage Approach
• STAGE 1 - KMeans (k=3): Finds 3 natural driving style clusters in the data
• No human labels needed — purely data-driven segmentation
• Clusters are mapped to: Eco / Moderate / Aggressive by energy usage
• STAGE 2 - Random Forest Classifier: Learns boundaries from KMeans labels
• Allows real-time scoring on new, unseen driving data
Input Features
• Vehicle Speed [km/h] — speed baseline
• Energy Consumption [Wh/km] — efficiency measure
• Engine RPM [RPM] — aggressive = high RPM at low speed
• Gradient — terrain correction for fairness
• Absolute Load [%] — throttle application intensity
• Terrain_Corrected_Energy = Energy / (1 + |Gradient|)
Driving Style Signatures
• ECO: low speed, steady throttle, high energy efficiency, low RPM
• MODERATE: medium speed, occasional acceleration bursts
• AGGRESSIVE: high RPM at intersections, frequent 0-100km/h cycles
• class_weight='balanced' — handles rare Aggressive events fairly
• Output: Per-second classification + overall trip Eco-Score (%)
Real-World Applications
Fleet Management
Score every driver in a corporate EV fleet. Fire high-risk, high-cost aggressive drivers.
Insurance Telematics
Usage-Based Insurance (UBI): aggressive driver pays 30% higher premium automatically.
EV Warranty Claims
Prove or disprove that battery degradation was caused by driver behavior, not manufacturing defect.
Gamification
Show driver their Eco-Score improving in real-time. Motivates fuel-efficient behavior.
CAP_PROJ_2 | Electric Vehicle Intelligence Platform

## Slide 8
Feature 4: Road Hazard Risk Predictor
Model: Random Forest Classifier — NO Camera, NO Radar
Goal: Classify every road segment as Low / Medium / High hazard using ONLY OBD-II sensor data. Replicates a meaningful subset of expensive ADAS functionality at near-zero hardware cost.
Physics-Informed Hazard Labelling
• No ground-truth accident data exists in dataset
• Constructed labels from 5 compounding risk indicators:
• - Speed Excess above posted legal limit
• - Intersection proximity (binary flag)
• - Road gradient (steep = longer braking distance)
• - OAT < 4°C = Ice risk even without precipitation sensor
• - High Engine Load AT an intersection = aggressive entry
• Risk Score = weighted sum; mapped to Low / Med / High
Input Features (with Pearson r)
• Vehicle Speed [km/h] — primary accident cause
• Speed Limit [km/h] — computes legal excess |r| ≈ 0.45
• Intersection — highest-frequency accident location
• Gradient — braking effectiveness |r| ≈ 0.22
• Absolute Load [%] — aggressive throttle |r| ≈ 0.20
• MAF [g/sec] — rapid acceleration signal |r| ≈ 0.19
• Engine RPM — ICE/EV mode distinction |r| ≈ 0.18
• OAT [DegC] — ice risk proxy |r| ≈ 0.15
Market Differentiation
• Current ADAS: Camera ($1,200) + Radar ($800) + LIDAR ($5,000+)
• Our System: OBD-II port already in every post-2008 vehicle
• Scales to ALL existing vehicles, not just premium new models
• Works in heavy rain/fog where cameras and radar fail
• Dropped columns: Battery SOC, HVAC, Elevation (r < 0.05 each)
• Dropped: Speed Limit with Direction (r=0.98 collinear duplicate)
Risk Level Definitions
LOW
Speed ≤ limit, no intersection, flat road, OAT > 4°C. Physics: all safety margins positive.
MEDIUM
Slight speeding (1–9 km/h over), standard intersection, or steep gradient. Elevated caution zone.
HIGH
>10 km/h over limit OR high throttle at intersection OR ice-risk temperature. Collision-probable.
CAP_PROJ_2 | Electric Vehicle Intelligence Platform

## Slide 9
Feature 5: Battery Health & Degradation Risk Monitor
Model: XGBoost Classifier
Goal: Classify every telemetry row into Low / Medium / High battery stress. Track micro-degradation events in real-time — long before warranty failure or 'idiot light' activation.
Why XGBoost? (Not Random Forest)
• Battery degradation physics are highly non-linear & interactive
• 100A is safe at 50% SOC, 20°C — SAME 100A is critical at 10% SOC, -5°C
• XGBoost's sequential boosting finds these deep 5-variable interactions
• scale_pos_weight balances rare High-Stress events (only 7% of data)
• Random Forest treats all trees equally — misses rare dangerous spikes
• XGBoost specifically hunts and penalizes missed minority class errors
Input Features
• HV Battery Current [A] — high discharge = chemical stress
• HV Battery SOC [%] — extremes (< 15% or > 90%) = damage zone
• OAT [DegC] — cold = electrolyte viscosity increase
• HVAC_Total_Watts — engineered: combined HVAC thermal load
• Battery_Power_Watts = Current x Voltage — real power draw
• SOC_Extremity = |SOC - 50| / 50 — how far from healthy center
• Thermal_Stress = |OAT - 22| x |Current| / 100
• High_Discharge_Flag = 1 if |Current| > 90A
Stress Level Definitions
• LOW: SOC in 30–85%, moderate current, temperature 10–35°C
• → Battery chemistry fully stable, zero degradation risk
• MEDIUM: Moderate SOC extremity or elevated current draw
• → Normal EV operation, slight wear over years
• HIGH: SOC < 15% or > 90% + high current OR temp < 0°C under load
• → Active chemical damage (lithium plating / thermal runaway risk)
• Labelled via physics rules — no external damage dataset needed
The Battery Degradation Science Behind the Labels
• Lithium Plating: Charging too fast (high current) when battery is already >90% full deposits metallic lithium — permanently reduces capacity.
• Electrolyte Decomposition: Discharging fully (SOC < 10%) in freezing cold causes electrolyte to solidify, cracking the separator membrane.
• Thermal Runaway Risk: Pulling >100A at very low SOC generates internal heat exceeding 60°C, accelerating SEI layer growth and capacity fade.
CAP_PROJ_2 | Electric Vehicle Intelligence Platform

## Slide 10
Technology Stack & Implementation Details
Full-stack Python ML application
Streamlit
Web UI framework. Real-time drag-and-drop CSV upload, sidebar navigation, live streaming simulation.
Scikit-learn
Random Forest Regressor (F1), Gradient Boosting Regressor (F2), Random Forest Classifier (F3, F4), KMeans (F3 labelling).
XGBoost
Feature 5 Battery Health classifier. Handles class imbalance via scale_pos_weight. GPU-capable for production.
Pandas
Full ETL pipeline — column selection, fillna imputation, outlier clipping, feature engineering, train/test split.
Joblib
Model serialization. 3-5x faster and 60% smaller files vs. Pickle for NumPy-heavy sklearn models.
Plotly
Interactive charts: histograms, scatter plots (color-coded by class), timeline line charts, donut pie charts.
StandardScaler
Z-score normalization applied on train set, transform-only on test/inference set to prevent data leakage.
Subprocess
Auto-training orchestration: app.py triggers preprocessing + ml_model scripts in background on first launch.
CAP_PROJ_2 | Electric Vehicle Intelligence Platform

## Slide 11
Model Performance & Results
Evaluation metrics across all 5 features
Feature
Model
Primary Metric
Secondary Metric
F1: HVAC Optimizer
Random Forest Regressor
R² = 0.99
RMSE: ~45W
F2: Regen Braking
Gradient Boosting Regressor
R² = 0.97
RMSE: ~3.2A
F3: Driver Behavior
RF Classifier (on KMeans)
Accuracy: ~94%
Balanced F1-Score
F4: Road Hazard Risk
Random Forest Classifier
Accuracy: ~95%+
High Precision
F5: Battery Health
XGBoost Classifier
Accuracy: ~93%
High Recall on HS
Key System Achievements
✓ All 5 models train automatically on first launch via subprocess orchestration
✓ Full inference pipeline runs on any new uploaded CSV in < 2 seconds
✓ Physics-informed labelling eliminates need for expensive labeled accident/degradation datasets
✓ Handles 37-column messy real-world OBD-II data with robust imputation & outlier handling
CAP_PROJ_2 | Electric Vehicle Intelligence Platform

## Slide 12
Conclusion & Future Scope
From proof-of-concept to production EV intelligence platform
What We Proved
• Software-only ML can replicate expensive ADAS safety hardware
• OBD-II telemetry contains enough signal for 5 distinct predictive tasks
• Physics-informed labelling is a viable alternative to manual annotation
• Proactive HVAC throttling can extend range without driver awareness
• XGBoost catches rare battery stress events that tree ensembles miss
• Sensorless hazard detection works across all road types and weather
• Full auto-training pipeline requires zero manual model management
• Dashboard handles real-world messy CSVs robustly end-to-end
Future Scope & Extensions
• Deploy to Raspberry Pi mounted in real vehicle for live OBD-II streaming
• Add LSTM / Temporal deep learning for time-series sequence prediction
• Integrate GPS map overlay for route-based hazard mapping
• Cloud API deployment (FastAPI + Docker) for fleet telemetry aggregation
• Real accident data integration for supervised hazard model validation
• Multi-vehicle fleet dashboard with driver comparison leaderboards
• Mobile app (iOS/Android) for driver eco-score gamification
• Add weather API integration (precipitation, visibility) for F4 enhancement
• OTA model update system: models retrain weekly on new fleet data
CAP_PROJ_2 | Electric Vehicle Intelligence Platform

## Slide 13
Thank You
Electric Vehicle Sensor Analytics — Predictive ML Dashboard
5 Features | 5 ML Models | 37 Sensor Columns | ~500K Data Points | Zero Extra Hardware
Built with: Python • Streamlit • Scikit-learn • XGBoost • Pandas • Plotly • Joblib
CAP_PROJ_2 | 2026